## Slide 1
01
Design of an UR5 robotic manipulator in 20Sim
Modeling and Simulation of Mechatronic Systems
PRESENTED BY:
Francesco Baldassarre
Riccardo Legnini
Samuele Rosato

## Slide 2
Introduction to UR5
02
6 degree of freedom
Serial manufacturing
Handling materials
Tele-operations
Goal: design, control and simulate a 20sim model of the UR5

## Slide 3
Kinematic model
03
Describes how each link is positioned and oriented with respect to the previous one. Denavit Herterberg kinematic model has been exploited:
  A is the point of link i in which joint i is attached
  B is the point of link i in which joint i+1 is attacched

## Slide 4
  Inputs: linear and rotational velocities from the previous joint
  TF (R_alpha): transformation from the joint frame to the link frame
  Euler Equations Block: integration of the forces/torques to obtain the new position/orientation of G
  MTF: add the gravity force along the correct direction
  Outputs: linear and rotational velocities of point B
04
Link model

## Slide 5
Newton-Euler Equations:
Dynamic model
05
Takes into account the mass and the intertia of each link, to compute the actual movements when forces/torques are applied.
New rotation/position matrices
Velocities of the center of mass

## Slide 6
  Inputs: linear and rotational velocities from the previous link. Joint velocity (theta_dot) from the Harmonic Drive
  R_C Block: necessary to constrain the rotation about x and y, and the translational velocity
  0 Junction: sum of rotational velocity with joint velocity.
  R_AB: rotational matrix between frame of link i and link i+1
  Outputs: linear and rotational velocities of point B
06
Joint model

## Slide 7
Useful tool to reduce the angular velocity and enhance the torque coming out from an electric motor
Reduction gearbox
Harmonic Drive
07
  I port: needed to model the motor-side rotational inertial
  R ports: model the viscous friction inside the Harmonic Drive
  C port: models the torsional stifness of the Harmonic Drive
  TF: represents the reduction ratio

## Slide 8
Control action: PID
08
Derivative time constant
Tameness constant
Proportional gain
Integral time constant

## Slide 9
Results
PID
PID + gravity compensation
It is possible to notice that the two obtained results are similar for what concerns the asessment time.
Particularly interesting is the overshoot of theta3, which in the second case decreases thanks to the gravity compensation term.
09

## Slide 10
Thank You
For Your Attention